## Slide 1: Electrical measurements and signals
P. LeClair
PH 4/591 Fall 2022

## Slide 2: why?
Just about every measurement ends up being electrical at some point
General aspects and circuits
Signal processing
  Modulation techniques: improve S/N
  Grounding and other nefarious problems

## Slide 3: series resistors
-
+
R2
I
I
∆V
R1
a
c
b
Req
∆V
a
c
-
+

## Slide 4: voltage divider
R2
R1
Vin
Vout
Vout =
R2
R1+R2
Vin
signal
in
signal
out
R1
R2
volume

## Slide 5: parallel resistors
current divider
I
-
+
R1
∆V
R2
a
b
I1
I2
∆V1=∆V2=∆V
-
+
Req
∆V
Req R1 R2
1
1
1
=
+

## Slide 6: more complex arrangements

## Slide 7: Thévenin equivalents
any weird combinations of R’s and V’s
is equivalent
to a
SINGLE R and V
(or a single I source
in parallel with R)
Vth = V (open circuit)
Rth =
V (open circuit)
I (closed circuit)

## Slide 8: so what?
E
R
real sources =
ideal sources + R
real meter =
ideal meter with R
V
I
R

## Slide 9: V source loading
V
r
source
like a battery
Rload
∆Vload = V - Ir
for r ≪ Rload,
∆Vload ≈ V
V source wants R high
one easy solution:
large resistor in parallel with load
I

## Slide 10
Ip
I source loading
source
Rload
I source wants R low
sourcing currents at high Rload is hard
I
r
Iload
Iload = I
r
r+R
for Rload ≪ r,
Iload ≈ I

## Slide 11: measuring the meter
Rload
I
V
r
real
meter
Req
I
V
ideal
meter
∆Vload = IReq =
R
1+R/r
I
Rload ≪ r, ∆Vload ≈ IR

## Slide 12: summary
voltmeter wants R low!
  can use a buffer/follower
I source wants R low
  transformer pre-amp if ac
  consider sourcing V
V source wants R high
  large series + parallel resistors
  present large R

## Slide 13: Sourcing current
Rwires
Rwires
Rthing
I
V
This is what a hand meter does.
Why is it not great?
Vmeter = I(Rthing + 2Rwires)
Meters: check your inputs
Check for “R=0” by shorting leads
Keep after the batteries …

## Slide 14: Sourcing current, “properly”
No problem.
You just need four wires.
What is still potentially wrong?
Rwires
Rwires
Rthing
I
V
Rthing ≪ Rinternal
or add buffer

## Slide 15: source/meter impedance
voltmeter wants R low
  Buffer/amp to increase input R of meter?
  can easily provide ~1010 Ohm
I source wants R low
  can we stay in compliance? What does that mean?
  is it better to source V?
  pre-amp?
  High resistances are a problem
  But so are low resistances if V is too small!

## Slide 16: Sourcing voltage
Rwires
Rwires
Rthing
Vs
Still have to measure voltage on device
the wires have a V drop
What about current?
V

## Slide 17: Sourcing voltage II
R = ∆V / I
Note we need 4 wires again
current meter - not hard
still problems?
Rwires
Rwires
Rthing
Vs
V
Ι
Ι
=
Rprecise
V
Rpar
Rs

## Slide 18: source/meter resistances
voltmeter wants R low
but V source wants R high
need buffer/amp on V meter
resistor in parallel with source
if V source is problem, R is too low
  consider sourcing I

## Slide 19: what if I want to measure a small change in R?
V
R1
R3
R2
Rx+dR
Vs
Adjust R2 to balance to V=0
Detect small changes in V
At balance,
Allows very accurate difference measurement
(measure only the change not change + bkgd)

## Slide 20: what about a real sample with a weird shape? Van der Pauw technique
make four fairly arbitrary contacts
source I on 2 adjacent contacts
measure V on the other two
rotate the configuration 90o
solve a little equation …
get sheet resistance (resistivity/thickness)
<works for Hall effect too>

## Slide 21: What? Why?
no patterning!
  - we are lazy
  - separates material properties from processing
get sheet resistance
    (+ resistivity with known thickness)
get doping type (i.e. if it is a p-type or n-type) material.
get sheet carrier density of the majority carrier
    (+ doping level with known thickness)
get mobility of the majority carrier.

## Slide 22: rc circuits
R
C
S
V ∝ e-τ/RC
V
E
Do it on purpose: ramp/time delay
Time domain analysis …

## Slide 23: differentiator
C
Vin (t)
V (t)
R
for small RC,
}
Voltage across C is Vin-V
Same current in C and R

## Slide 24: integrator
C
Vin (t)
Vout (t)
R
for large RC (V ≪ Vin)
}

## Slide 25: so what?
On purpose: filtering of signals
Not on purpose:
                unintentional capacitive coupling
                see from waveform shape
                debugging tool …
more later

## Slide 26: ac circuits & impedance
generalization of resistance to time-varying signals
using ac, everything lets current through a little
Z = impedance ~ resistance
  frequency dependent
  can include phase shift! (time lag of V or I)
ZR = R
ZC = -i/wX
ZL = iwL
}
+/- 90o phase shift

## Slide 27: resistive circuits
nothing earth-shattering happens
except P is lower than you expect

## Slide 28: capacitive circuits
I and V 90o out of phase
average power is ZERO
frequency response?
  insulating at dc
  conducting at high f
voltage “lags” current

## Slide 29: our filters in frequency domain
C
R
Vin
Vout
low-pass
C
Vin
Vout
R
high-pass

## Slide 30: familiar?
low-pass filter
C
R
Vin
Vout
C
Vin
Vout
R
high-pass filter
differentiator
integrator
frequency domain
⇕
time domain

## Slide 31: familiar?
low-pass filter
C
R
Vin
Vout
C
Vin
Vout
R
high-pass filter
differentiator
integrator
frequency domain
⇕
time domain
Cut out high frequency noise
Smooths (but slows response)
Eliminate slow variations
Magnify changes
Peaks become zero crossing

## Slide 36
dB/decade ...

## Slide 37
audio crossovers

## Slide 38
inductive “kick” …
aka the Angry Current

## Slide 43: noise
Frequency dependence of noise
Low frequency ~ 1 / f
  example: temperature (0.1 Hz) , pressure (1 Hz), acoustics (10 -- 100 Hz)
High frequency ~ constant = white noise
  example: shot noise, Johnson (thermal) noise, spontaneous emission noise
Total noise depends strongly on freq.; worst at DC, best in “white” region
Problem -- most signals at DC
  (Bandwidth? Measurement time)
log(Vnoise)
log( f )
Noise amplitude
1/f noise
0
White noise
0.1 1 10 100 1k

## Slide 44: what’s your bandwidth?
log(Vnoise)
log( f )
Total noise in 10 Hz bandwidth
1/f noise
0
White noise
0.1 1 10 100 1kHz
Signal at DC
10 Hz
log(Vnoise)
log( f )
1/f noise
0
White noise
0.1 1 10 100 1kHz
Signal at 1 kHz
10 Hz
if we could just measure only one frequency in a narrow bandwidth ...
and shift our measurement to higher frequency ...

## Slide 45: No, what is bandwidth?
2 key frequencies:
- inverse of measurement time T sets low f
- sampling frequency is high limit
Shannon-Nyquist theorem: bandwidth is ½ sampling frequency. Measure at 1kHz sampling, BW=0.5kHz.
“If a function x(t) contains frequencies no higher than fmax, it can be completely determined by sampling a series of points spaced T=1/2 fmax seconds apart, i.e., by sampling at a rate of 2fmax samples per second.”

## Slide 46: how do we make a signal periodic?
Modulate signal, but not noise ... far from 1/f
  no universal technique
  optical chopper wheel, freq modulation
  small modulation voltage on dc ramp
  Freq low compared to phenomena of interest,
  outside known noisy bands
Shifts signal out to higher frequencies
Detect only at modulation frequency
  Noise at all other frequencies averages to zero
  odds that stray signals are at this f?
  controlled perturbation ... linear response

## Slide 47: then what?
dc + reference f drives system
multiply response by reference
(can add phase adjust so one is zero)

## Slide 48: Demodulation / Mixing
Sum and difference freq generated
Interference, basically
If signal frequency is close to reference frequency:
  low frequency “beating”
  product is DC if signal & ref. have same frequency
  take product, filter, integrate over time
  magnitude depends on relative phase

## Slide 49: so what?
pass signal through a low pass filter – all ac signals gone
In general, nothing is left …
but if input and signal frequencies match, first term is dc!
Can set ref phase to zero
Very narrow bandwidth (~0.1Hz)
Demodulated signal
After multiplying
Voltage
time
plus low pass

## Slide 50: Signal freq approaches ref freq
Beat frequency approaches DC as signal freq approaches ref freq
1
1.05
1.1
1.15
1.2
1.25
Signal freq
vs ref freq
Reference
Mixer outputs
}
caught by filter
+
integrate to zero!

## Slide 51: block diagram
Key: sin waves are orthogonal unless f’s match
product of ref + modulated response = dc if f’s match
low-pass = averaging (integrating) + remove harmonics
can set time constant to vary degree of rejection/bandwidth
bandwidth tiny ... ~mHz ... very low noise!
add phase shifter to reference ... tune to max output
Output
Demodulated signal
After mixer
Voltage
time
After mixer & low pass
Ref
Input
Mixer
Low pass
filter
Buffer
Phase
shift f

## Slide 52: Slightly more realistic

## Slide 53: another description
what we really do is multiply sig & ref and integrate
  low-pass = integrator
  T = “time constant”
orthogonality of sin waves:
  sin wave input, integral non-zero only if freq’s match
  practically zero for T ~ 5/f (wait ~5 time constants)
  Non-linear response: Fourier series, etc.

## Slide 54: math is useful
resulting signal is essentially DC
contribution from any signal not at fref is nearly 0
out-of-phase component at fref also nearly zero
    sin and cos are also orthogonal
“phase sensitive detector”

## Slide 55: example: measuring dI/dV
‘blow up’ small changes in current/conduction
numerical differentiation of I(V) ?
  discretization noise
  RC integrator too restricted
drive system with dc ramp + ac modulation
measure response at modulation frequency
we need a frequency / phase sensitive technique

## Slide 56
How big should δV be?
ac modulation gives average dI/dV
  over [V - δV, V + δV]
  features smaller than 2δV not resolved
thermal broadening of Fermi-Dirac
  “smearing” over E window ~ 3.5kBT wide
choose δV < 3.5kBT (when you can)

## Slide 57: What should the frequency be?
many devices ~ capacitor || resistor
    want to neglect ZC … not too high
    capacitance gives “parasitic” modulation
    want reasonable measure times … R*C
    nowhere near 60Hz (or harmonics)
In practice: ~Hz – kHz
    (very, very slow for electrons)

## Slide 58: realistic circuit

## Slide 59: grounding and other problems

## Slide 60
other problems I: imperfect equipment
Finite input impedance
Finite output impedance
A/D converter (resolution)
discretize signal
12 bit = 212 = 4096 +/- 5V Þ 2.4mV res.
16 bit = 216 = 65536 +/- 5V Þ 0.15mV res.
    Þ pre-amps, offset techniques (e.g., bridge)
Time constants
~ several time constants between points
compare to frequency used
consider instrument and device response (RC)
    Þ averaging of some sort - point, sweep/ensemble, multichannel

## Slide 61
other problems II: ‘pickup’
Inductive coupling
Sources of B(t) ???
Light bulbs …
CRT …
everything that plugs in
Avoiding?
Twisted pair wiring
Capacitive coupling
Sources?
you touching cables
proximity of cables
cables having the audacity to exist
Avoiding?
coax (partly)
be very, very still …

## Slide 62: So this means?
Coax is terrible.
    Inductive pickup. B(t) only attenuated
    Helpful: high permeability (magnet sticks to it) shielding
Twisted pairs are terrible
    Capacitive pickup. E(t) is not shielded
    Helpful: conductive shielding
Triax? Why not?
Twisted pairs in a coax = OK*
  *cheaper: you can just twist two coax cables
  the electrons don’t know the difference

## Slide 63
… and then there are ground loops (resistive coupling)
ground everything to the same SINGLE point
“V=0 at ground” is an electrostatics statement, it is not dynamically true
shielding ¹ ground
trial and error
don’t forget: 60Hz is *everywhere*
This is the
HARDEST
problem
Note that instruments are often poorly spec’d. Is the outer part of the BNC ground or not?
anything

## Slide 64: “other”
Microphonics
  touch nothing.
  deformation of coax Þ change C
  Yes, you can see this effect
Thermocouple effects
  choose your wire carefully
  Light ballasts put out weird frequencies.
  Switching mode power supplies are ghastly