## Slide 1: Process and measurement control
P. LeClair
PH 4/591 Fall 2022

## Slide 2: General scheme
Monitoring of processes and operations
Control of processes and operations
Experimental engineering analysis

## Slide 3: Monitoring
Sometimes we’re just watching
  Thermometer, barometer for weather
  Just indicate condition, no control function
Maybe you can’t control it
Maybe you aren’t sure you need to
  Recording just in case

## Slide 4: Control
Measuring instrument serves as part of control system – e.g., sweep x and measure y
Clearly: to regulate a variable, must measure it
Feedback is at the heart. e.g., thermostat
Endless variety.
Distinction not always clear:
  Monitoring for one may be control for another
  Weather: we monitor, farmers use as control

## Slide 5: Control (closed loop)
Process
Final control element
Measuring instrument
Controller
Controlled
variable
Input energy and/or material
Desired value of controlled variable
Disturbances

## Slide 6: Experimental engineering analysis
“engineering” = “actually doing the thing”
Point is to solve a problem
Both theoretical and experimental problem-solving methods used in concert
Some general points follow

## Slide 7: Theoretical methods
Results often for general rather than restricted case
Necessarily require simplifying assumptions: modeling is always different from reality
Math may be complicated ... numerical only
May require extensive computing but not lab space …
Smaller time delay associated compared to experiment
  (no setup/acquisition/etc)

## Slide 8: Experimental models
Often specific to system under study (generalization possible but limited)
No simplifying assumptions needed – can run on actual system
Require accurate measurements – can be expensive or complicated …
Actual system or scale model required
Considerable time required to design/build/debug

## Slide 9: Types of experimental-analysis problems
Test validity of a theoretical prediction
Formulate generalized empirical relationship where good theory does not exist (e.g. fluids)
Determination of parameters for material, component, or system (e.g., efficiency)
Study of phenomena to help develop theory
Solution of equations by analogy (e.g., solid state gravitation analogues)

## Slide 10: Description of Instruments
Describe generally the operation and performance without reference to specific hardware
Operation in terms of functional elements
Performance in terms of static & dynamic characteristics
Recurring themes  generalization
No single way to do it

## Slide 11: Possible arrangement of elements
Possible arrangement of functional elements in an instrument
Includes all necessary for basic function
Measured medium
Primary sensing
Variable-conversion
Variable manipulation
Data transmission
Data presentation
Data storage & playback
Observer
Measured
quantity
Presented data

## Slide 12: Primary sensing element
1st to receive energy from measured medium
Output depending in some way on measured quantity
Always extracts energy from medium
  Ideal measurement not possible
Measured medium
Primary sensing
Variable-conversion
Variable manipulation
Data transmission
Data presentation
Data storage & playback
Observer
Measured
quantity
Presented data

## Slide 13: Variable conversion element
May need to convert output of primary sensor
E.g., I to V, V to f, x to V
This is an abstraction – a physical instrument or module might have multiple functions in one
Measured medium
Primary sensing
Variable-conversion
Variable manipulation
Data transmission
Data presentation
Data storage & playback
Observer
Measured
quantity
Presented data

## Slide 14: Variable manipulation element
May need manipulation of output, e.g., size
For example: amplifier
May go before or after conversion element (or both)
Measured medium
Primary sensing
Variable-conversion
Variable manipulation
Data transmission
Data presentation
Data storage & playback
Observer
Measured
quantity
Presented data

## Slide 15: Data transmission/ storage / presentation
Transmission: functional elements may be physically separated
Anything from a rotating shaft to satellite telemetry
Presentation: make human readable
Measured medium
Primary sensing
Variable-conversion
Variable manipulation
Observer
Data transmission
Data presentation
Data storage & playback
Measured
quantity
Presented data

## Slide 16: Example: spring pressure gauge
Could transmit pressure with a small tube
Measured medium
Primary sensing
Variable-conversion
Data transmission
Data presentation
Observer
Measured
quantity
Presented data
Fluid
Piston
Piston
rod
Spring
Variable manipulation
Variable manipulation
Linkage
Pointer and scale
force
force
motion
motion
Schematic: Doebelin

## Slide 17: Methods for correcting interfering & modifying inputs
FI
FD
FM,I
FM,D
+
+
o
Output
Desired input
Modifying input
Interfering input
iI
iM
iD
Output component due to
interfering input and iM
Output component due to
desired input and iM

## Slide 18: Inputs
Desired inputs – quantities instrument is intended to measure
Interfering inputs – quantities it is unintentionally sensitive to
F = function that maps input to output
  Could just be a constant gain multiplier K
  Could be statistical. Could be complicated!
Modifying inputs – cause a change of input/output relationship. E.g., FM,I = how iM affects FI
Add all contributions to create actual output

## Slide 19: Strain gauge
Ideal gauge characteristic: change in R prop to strain
Image: Doebelin

## Slide 20: Strain gauge
Put in bridge configuration
Image: Doebelin

## Slide 21: Issues
Interference: 60Hz field – pickup in loops!
Gauge temperature modifies RG
Differential thermal expansion of gauge and specimen
Battery voltage changes and fluctuations
How to correct for or minimize these things?
  General idea leads us to feedback and control schemes

## Slide 22: Inherent sensitivity method
Duh: make the measurement only sensitive to what you want and not other things
Make FI and/or FM,D as near zero as possible
  So even if iI and iM exist they don’t affect output
Low thermal coefficient of R for gauge
Small thermal expansion coefficient
Twisted pair wiring / shielding to nullify 60Hz pickup
https://www.guralp.com/howtos/differential-v-single-ended.shtml

## Slide 23: Common mode signals – shielding is also key
Individual pairs can also have common pickup
Common mode signals hard to get rid of
https://www.maximintegrated.com/en/design/technical-documents/tutorials/2/2045.html

## Slide 24: Method of high-gain feedback
Measure voltage ei by feeding it to a motor whose torque is applied to a spring -> displacement xo.
Open-loop system (don’t monitor output, just run)
  This is what we generally seek to avoid.
All modifying inputs (iM’s) seen in output
Errors in direct proportion to gain of each element

## Slide 25: Open-loop system
KMo
FM,D,1
Voltage
iM,1
ei
Motor
KSp
FM,D,2
Torque
iM,2
Spring
Displacement
xo
Think about error propagation …
Voltage to measure – applied to motor, torque causes spring to compress, which moves an indicator

## Slide 26: Closed-loop system
Amplify original signal – draw less from medium
Feed part of output back to input as a difference
Output swings push back on themselves!
Constant gain on feedback:
KAm
FM,D,3
iM,3
ei
Motor
Spring
xo
KMo
Amplifier
KSp
FM,D,1
iM,1
FM,D,2
iM,2
+
-
eo
FM,D,4
iM,4
KFB
Feedback Device

## Slide 27: Closed-loop system
Check the math … what is different?
Output depends on itself … rearrange
So what? Output still linear in input signal at least …

## Slide 28: Method of high-gain feedback
Make KAm very large, such that
Now only feedback shows up – only it needs to be constant and unaffected by iM4. Easier!
Feedback is key, not the gain being especially large

## Slide 29: Method of high-gain feedback
Amp supplies most of the power, so feedback can work with low power
  Better accuracy and linearity, easier
Feedback can use tiny signals so influence on medium is much less than open-loop
Open loop is susceptible to all spurious inputs for all blocks, but all can be negated at once with high amplification and stable, accurate feedback
Familiar if you’ve used op-amps or transistors

## Slide 30: Feedback example
Operational amplifier (“op amp”)
Rules:
  Does what it must to keep V+=V-
  V+ and V- inputs draw no current
  Output limited by Vs+/-
  Open loop gain AOL huge (> 105)
  Too large to be useful (or stable)
  Would just swing between +/- Vs
https://commons.wikimedia.org/wiki/File:Op-amp_symbol.svg#/media/File:Op-amp_symbol.svg

## Slide 31: Feedback example
Op amp – inverting amp
Add feedback and close loop
Lowers gain but predictable and stable
https://commons.wikimedia.org/wiki/File:Op-Amp_Inverting_Amplifier.svg#/media/File:Op-Amp_Inverting_Amplifier.svg
V+ is at ground, so must be V-
- input draws no current
Current due to Vin across Rin must be same as current due to Vout across Rf, but in opposite direction!

## Slide 32: Feedback example
Output is inverted, with gain of Rf/Rin!
Open-loop gain of op-amp is irrelevant
Amp is easily swapped with another, not sensitive to gain fluctuations
https://commons.wikimedia.org/wiki/File:Op-Amp_Inverting_Amplifier.svg#/media/File:Op-Amp_Inverting_Amplifier.svg

## Slide 33: Noise
Open loop: eo = G(ei+Ns)
Noise alone: set ei=0, No = NsG
Noise is amplified, as expected
Signal to noise ratio in = SNRi = ei/Ns
Signal to noise ratio out = SNRo = eo/No = 1 + ei/Ns
SNR improved; use a low noise amp!
But … large power gain & low noise are not often compatible.
Two stage solution: low noise preamp, then high power amp
  Low noise and very high amplification not always possible either
ei
Noise source
eo
G
Ns

## Slide 34: Noise: dual amp - low gain low noise stage 1
Still open loop: eo = GaGbei presume amp a has minimal noise
Noise alone: set ei=0, No = NsGb
Noise is amplified by 2nd stage, as expected
Signal to noise ratio out = SNRo = eo/No = Gaei/No =Ga SNRi
Better SNR, as expected – just need 2 amps
Ga
ei
Noise source
amp b
High power
High gain
eo
amp a
Low noise
Gb
Ns

## Slide 35: Noise in feedback systems
Closed loop:
Noise alone:
Ga
ei
Noise source
amp b
eo
amp a
Gb
Ns
+
-
eo
Gf
Feedback Device
eo
Again, amp a helps
GfGaGb >>1 ?
No ~ Ns/GfGa !
very strong noise reduction!
Better SNR and retain benefits of feedback
Low-noise amp should be first and ASAP in signal chain

## Slide 36: Filtering
What it sounds like. On input or output (or both)
Consider signal as having many frequency components, squash the ones you don’t want
E.g., equalizer -> tweeter/woofer
FI
FD
FM,I
FM,D
+
+
Output
iI
iD
Zero
Filter
iI’
iM
Zero
Filter
iM’
On input or output
Input filtering shown

## Slide 37: Filtering
Can be electrical, mechanical, optical, etc.
Image: https://doi.org/10.1016/j.neuron.2019.02.039

## Slide 38: Examples
Mechanical: spring only couples a portion of vibration
Tilt angle filter: gimbal so tube always hangs vertical
Thermal isolation: nullify changes not due to T
Magnetic shield – no pickup
Image: Doebelin

## Slide 39: Passive RC output filter
Low-pass filter to attenuate 60 Hz pickup
Would want this before amplifier most of the time
  (why?)
Image: Doebelin

## Slide 40: Pneumatic filter
Restriction = pneumatic filter (low pass)
  Like RC filter in previous; only low freq. couple
Image: Doebelin

## Slide 41: Chopper
Modulate to shift measurement to less noisy frequency range and reduce bandwidth (LED blinking expt.)
Modulate faster than drift.
What are the odds anything moves at this frequency?
Basis for lock-in amplifier - later
Image: Doebelin

## Slide 42: Method of opposing inputs
Like active noise cancellation: if you can’t avoid the modifying input, sample it and add back out of phase
Idea clear for many decades, having signal processing hardware able to do it effectively and cheaply is another thing
Patent 1936. Commercial: 1980s
FI1
FI2
+
-
iI1
iI2
FD
iD
oI1
oI2
Output
o
oD
Unavoidably interfering input
Intentionally introduced interfering input
Desired input
+
+
oI2 - oI2
Essentially
zero

## Slide 43: Process control (PID)
Say you want to measure resistance vs temperature
You have a sample heater to control temperature
How do you do it? Closed-loop, but details
  How to ramp power to approach set point?
  Does overshoot matter (hysteresis)?
  Speed vs accuracy tradeoffs
How well you control process variable impacts the measurement of interest ...

## Slide 44: PID
Control process variable (PV) in comparison to setpoint (SP)
Error value e(t) is the difference, used to correct – closed loop
Image: http://commons.wikimedia.org/wiki/File:PID.svg
SP = desired = r(t), PV = actual output = y(t)
SP-PV = error = e(t), control function = u(t)

## Slide 45: Proportional
Control signal has 3 terms in response to error
P term = proportional
  Proportional to (SP-PV) via gain factor KP
  Like closed-loop example earlier
  Large (+) error => large (+) output
  Using P alone generally results in an error, because it requires an error to respond! No error, no response
  Does not account for nature of the deviation
  Sometimes P alone is enough
    (or even less than this: “bang-bang” controller = only on/off)
    (e.g., pulse width modulation)

## Slide 46: Integral
I term = integral
Integrates difference signal e(t) over time to respond
Eliminate offset / residual error
Historic accumulation matters
As error ↓ P is less effective … but I effect grows
Time scale: oscillations faster than 1/t don’t show up
Too high: overshoot at small e, leading to oscillation
General: feedback too high can lead to instability

## Slide 47: You guessed it, Derivative
Based on current rate of change
“anticipatory” control; damping
Correct for approaching SP too quickly/slowly
Basically, a damping/viscosity term
Purely derivative control cannot bring to SP – not sensitive to actual value of PV

## Slide 48: PID control
Tuning: find the K values to optimize response
  Always some trial and error – change SP and observe
  What do you mean by “optimum” …
  Rise vs settling time, overshoot, max dev?
Control action – as shown = “direct action”
  i.e., 100% error => 100% control signal
  Can be reverse action, e.g., valve 100/0% => 0/100%
Some applications need only 1 or 2 terms
  Natural damping/time constant of system
  Not D alone – sensitive to noise
  Need I to settle at longer times

## Slide 49: Math
Overall control function:
K’s are all non-negative (but can be zero)
Standard form, making timing explicit:
TI = how long you tolerate begin above/below SP … low-pass
TD = time with which controller attempts to approach SP … high-pass

## Slide 50: Control loop example: robotic arm
Can be moved and positioned by a control loop.
An electric motor lifts or lowers it based on power input
But: motor power can’t be a simple function of position due to mass of arm & forces on it (and need to be gentle!)
The sensed position is the process variable (PV).
The desired position is called the setpoint (SP).
The difference between the PV and SP is the error (e) – is the arm too low or too high & by how much.
The input to the process (motor current) is the output from the PID controller. Called manipulated variable (MV) or the control variable (CV).
By measuring the position (PV), and subtracting it from the setpoint (SP), the error (e) is found, and from it the controller calculates how much electric current to supply to the motor (MV).
https://en.wikipedia.org/wiki/PID_controller#Control_loop_example

## Slide 51: Effect of P,I,D on step response
At t=0, step change of input from 0 to 1
P increases the speed of the system, decreases the residual steady state error but cannot eliminate it
I eliminates the residual error but adds oscillations/overshoot
D “damps out” the undesired oscillations in the transient response.
GIF: https://en.wikipedia.org/wiki/PID_controller#/media/File:PID_Compensation_Animated.gif

## Slide 52: P alone (fix I, D)
Red: near critical damping (but slow)
Blue, green: P too high, overshoot
(but faster settle)
All curves: I too low, system tends to oscillation – always overshoots
(but fast settle if P high enough)
Increase P: rise time less, overshoot more; settling time similar; degrades stability …
Ask about the python code! Based on https://www.halvorsen.blog/documents/programming/python/resources/powerpoints/Python%20for%20Control%20Engineering.pdf

## Slide 53: I alone (fix P, D)
Green: near critical damping
Red, green: integral gain too high, oscillates (integration time too low compared to oscillation period)
Increase I / decrease TI: faster rise but more oscillation/overshoot
- like a low-pass filter

## Slide 54: D alone (fix P, I)
https://commons.wikimedia.org/wiki/File:Change_with_Kd.png#/media/File:Change_with_Kd.png
Increase D / increase TD: damp oscillation, decrease overshoot, similar rise time.
Small Kd can improve stability … but high frequency noise is a problem
Adding derivative helps, but clearly P/I are not tuned well

## Slide 55: PID
High P gain can lead to instability, but low P can make system unresponsive – action may be too small to respond to a disturbance
Best practice: bulk of response should be P
I can cause overshoot, but gets rid of offset from P alone
D term tries to predict behavior and improve settling time and stability. Often also needs low-pass filtering to limit susceptibility to high frequency noise
D is more seldom in practice – often P or PI alone. Actual behavior tough and impact on stability is tricky.

## Slide 56: PID
Doesn’t guarantee optimal control or control stability
  E.g., measurement of PV delayed, action too slow
  May need additional meas. or revise action
May be embedded in measurement loop
  E.g. PID to set T, only proceed when within tolerance
There is an open-loop way to do this – feed forward
  Control changes based on modeling rather than output
Can cascade – inner / outer or fast / slow combos
  E.g., cryogenics – may monitor several temperatures
  Gradient to outside also informs control

## Slide 57: Tuning
You want system critically damped – smooth decay to SP with no oscillation
Modern systems have autotuning features
Can do it manually, but not fun
Table:wikipedia/PID
Parameter | Rise time | Overshoot | Settling time | Steady-state error | Stability
Kp | Decrease | Increase | Small change | Decrease | Degrade
Ki | Decrease | Increase | Increase | Eliminate | Degrade
Kd | Minor change | Decrease | Decrease | No effect in theory | Improve if Kd small
Effects of increasing a parameter independently

## Slide 58: Tuning
Somewhat more clever: Ziegler–Nichols method
Set KI and KD gains to zero.
Increase KP until it reaches ultimate gain Ku and loop output starts to oscillate constantly.
Ku and oscillation period Tu are used to set the gains:
Table:wikipedia/PID
Control Type | Kp | Ki | Kd
P | 0.50Ku | — | —
PI | 0.45Ku | 0.54Ku/Tu | —
PID | 0.60Ku | 1.2Ku/Tu | 3KuTu/40

## Slide 59: references
“Measurement Systems: application and design”, Ernest O. Doebelin
https://en.wikipedia.org/wiki/PID_controller
https://en.wikipedia.org/wiki/Operational_amplifier
https://en.wikipedia.org/wiki/Operational_amplifier_applications
http://brettbeauregard.com/blog/2011/04/improving-the-beginners-pid-introduction/
Alain de Cheveigné, Israel Nelken, “Filters: When, Why, and How (Not) to Use Them”, Neuron 102, 280-293 (2019). https://doi.org/10.1016/j.neuron.2019.02.039.
https://www.halvorsen.blog/documents/programming/python/resources/powerpoints/Python%20for%20Control%20Engineering.pdf
https://www.allaboutcircuits.com/technical-articles/negative-feedback-part-3-improving-noise-linearity-and-impedance/